## Slide 1: SDN-BASED MALICIOUS NETWORK TRAFFIC DEFENSE SOLUTION
Team: 15
ClassID:14,18,19, 36

## Slide 2: PROJECT MOTIVATION
SDN Advantages : Centralized, Flexible, Programmable, Scalibility
Security: Cyber Attack -> Network Mapping
Monitoring real-time statisitcal flow chart
2. Fake Listening host with almost no cost
3. Block, Redirect flow to fake listening host

## Slide 3: DDOS
Type: HTTP, TCP sync, UDP, ICMP packets
Multi-Attackers
block web services with large amount requests
Hard to detect in very beginning

## Slide 4: ENVIRONMENT
Network Devices: Mininet in VM - topology
Controller: Floodlight - global view
Network Monitor: sFlow - collect statistics
Protocol: OpenFlow1.3
REST API

## Slide 5: TOPOLOGY
Malicious Hosts
bait Server
Server

## Slide 6: TOPOLOGY
Floodlight Controller
Malicious Hosts
Server

## Slide 7: TOPOLOGY
Floodlight Controller
REST API
Malicious Hosts
Server

## Slide 8: REST API APPLICATION
Over Http request (GET/POST)
Recommended way to implement first floodlight app
But…
Limit and version dependent

## Slide 9: FLOODLIGHT MODULE
Current floodlight modules do not meet our needs
Create our own modules
  Monitor ICMP Echo Request
  Monitor TCP or UDP Request
  Monitor HTTP GET of POST Request
How to develop a flood module
  Inherit from IOFMessageListener, IFloodlightModule
  Implement Resource class to provides data to applications
  Implement Routable class to provides REST API
  Define Serializer class to generate Json

## Slide 10: HeaderExtract
A floodlight module
Developed by ourselves
Monitor ICMP
Monitor TCP or UDP Request

## Slide 11: HTTPFilter
A floodlight module
Developed by ourselves
Monitor HTTP Request
Drop specific IP HTTP Request

## Slide 12: MININET
Realistic Virtual Network on VM, cloud, anywhere
Deploy Networks a click with Scripting Language
Ideal experiment environment with OpenFlow and Software-Defined Networking

## Slide 13: PROJECT GOAL
Develope an REST API application with Floodlight Controller
Methodology:
Monitoring the flow with src-dst pairs
DDos detected, send flow rule on sentinel switch Redirect malicious traffic to fake hosts

## Slide 14: SCENARIO
Floodlight Controller
sentinel switch
sentinel switch
icmp ddos
tcp ddos

## Slide 15: FLOW TABLE IN SENTINEL SWITCH
ipv4_src | ipv4_dst | ip_proto=0x06 (TCP) | ip_proto=0x11(UDP) | icmpv4_type=8(ICMP) | tcp_dst=80(http)
10.0.0.1 | 10.0.0.8 |  |  | 51 | 
10.0.0.2 | 10.0.0.8 |  |  |  | 349
10.0.0.3 | 10.0.0.5 |  |  |  | 
10.0.0.1 | 10.0.0.5 |  |  |  | 

## Slide 16: PSEUDO CODE
if ip_src && ip_dst not in hash_table: hash_table[ip_dst][ip_src-ip_dst]->counter =0 ddos_table[ip_dst]++ hash_table[ip_dst][ip_src-ip_dst]++ for ddos_count in ddos_table: if ddos_threshold > threshold: switches = get_route_switch(ip_src, ip_dst) apply_redirect(switch, ip_src) for switch in switches apply_block(switch, ip_src) for switch in switches
match field can be TCP/UDP/ICMP/TCP_port

## Slide 17: SCENARIO
Floodlight Controller
Forward Flow Rule!
tcp ddos
DDos Detect!

## Slide 18: SCENARIO
Floodlight Controller
Redirect
tcp ddos
DDos Detect!

## Slide 19: TOPOLOGY

## Slide 20: Flow Chart

## Slide 25: CONCLUSION
Floodlight modules provide REST API to develop application but limited
You can contribute your module to Floodlight!

## Slide 26: DEMO